## Slide 1: Root Cause Analysis Report
Horizontal Cartoner – Downtime & Spare Parts Review (July 2025)

## Slide 2: Executive Summary
• The Carton Feed System is the dominant cause of downtime.
• It accounts for 496 occurrences and over 18,215 units of downtime.
• This was validated against spare parts replaced (flat belts, strips).
• Manual references confirm complex interlinking of carton, suction, and servo systems.

## Slide 3: Data Sources & Inputs
1. Downtime Logs (Book2.xlsx)
- Issue descriptions, frequency, downtime
2. Spare Parts Consumption (Book3.xlsx)
- Material descriptions, dates, quantity
3. Machine Manual (PDF)
- Lists of motors, sensors, alarms, critical components

## Slide 4: Key Downtime Component
🛠️ Component: **Carton Feed System**
• Frequency: 496
• Cumulative Downtime: 18,215 units
• Tags matched via: belt, pick, insert, strip, vacuum, carton, magazine

## Slide 5: Spare Parts Supporting the Diagnosis
• Flat Belt PT 1.5 O-G3 – 3 units replaced in May 2024
• Soap Pocket Strip – 50 units replaced
• Validates mechanical wear & jam issues in carton feed

## Slide 6: Failure Modes in Carton Feed System
• Belt: Slippage, misalignment, tearing
• Vacuum: Loss of suction, MPCB trips
• Servo/Encoder: Mis-synchronization, incorrect angles
• Carton Strip: Misfeed, buckling, wear
• Magazine: Jamming or improper loading

## Slide 7: Final Inference & Recommendations
• Carton Feed System is the key downtime driver
• Validated through downtime data, spare parts, and manual inspection
• Recommendations:
- Periodic belt & strip inspection
- Suction leak checks
- Servo & encoder calibration
- Improve strip loading SOPs